## Slide 1
Concepts and Configuration Workshop
Dell Force10 Network Switches

## Slide 2: Quantum’s Lattus Object Store uses Dell Force10 network switches
The Lattus installation guide provides Dell switch configurations based on rack and system switches used by Lattus. The basic “standard” configurations are generally defined but does not cover all configuration possibilities. This workshop references Dell FTOS commands and FTOS-SI emulator to teach you how to configure Dell’s Force10 Network switches.
This workshop does not replace the Lattus installation Guide.
Use for reference only.

## Slide 3: Downloading and installing the Dell Networking OS Emulator
The Dell FTOS Emulator and Users Guide is available at:
http://www.cocheno.com/2015/08/dell-ftos-emulator/
The Users Guide uses Oracle VM Virtual Box:
https://www.virtualbox.org/
Note: VMware works as well but is not covered in the Users Guide.
User Guide for Dell Networking OS Emulator is included in the presentation zip file.
FTOS Configuration Guide is included in the presentation zip file. This guide is a good resource providing definitions and standards for each command.

## Slide 4: General Switch Information
All ports must resided in a vlan, the default vlan 1 cannot be removed.
Ports within the default vlan can remain disabled = shutdown.
Manage ports by (untagged) or (no untagged) within the vlan by interface.
Add a ? to the end of the command to see the next available commands.
Use “no” preceding the command to do the opposite.
>wr to save
>copy running-config startup-config
>show logging

## Slide 5: General Switch Information
To manage the switch “privileged” mode, type (enable) and enter the password if set. Quantum’s default is password.
Most commands require configuration mode (conf) to execute. Type (conf)
The show commands are ran at root level. When in conf mode you can run show commands by adding (do) to the beginning of the command. >(conf) do show run
Use the show run command to see the switch configuration and port types.
Type exit to return from the current configuration mode.
Initial configuration is thru the console serial port R45 to RS-232. Some switches have USB access as well, the ports behave the same.

## Slide 6: Initial Configuration
Set clock>time and date:
>clock set 14:45:00 30 June 2017
>clock timezone Central -6 (Note: This command is not supported with the Emulator)
>show clock
Set hostname:
>(conf) hostname Force10
Set Password/Privilege:
>(conf) username admin privilege 15 password 0 password
>(conf) enable password level 15 0 password

## Slide 7: Initial Configuration
Set SSH/Telnet:
>(conf) ip ssh server enable
>(conf) ip ssh rsa-authentication enable
>(conf) ip ssh server version 2
Set lldp:
>(conf)#protocol lldp
>(conf-lldp)#advertise management-tlv system-capabilities
>(conf-lldp)#no disable
>(conf-lldp)#exit

## Slide 8: Initial Configuration
Configure a management port:
>show interface management 0/0
>(conf) interface managementethernet 0/0
>ip address 192.168.1.2/24
>no shutdown
>exit
Review the configuration:
># show run
>(conf) do show run

## Slide 9: Configure an Interface
To configure an interface use the interface command specifying which interface port number:
>(conf) interface fortyGigE 0/12
>(conf-if-fo-0/12) show config
For a Lattus rack switch we would configure the 1G ports with the following options:
>(conf-if-fo-0/12) switchport (Places the ports in layer 2 mode)
>(conf-if-fo-0/12) no ip address (No ip assigned)
>(conf-if-fo-0/12) spanning-tree rstp edge-port (Edge devices only)
>(conf-if-fo-0/12) flowcontrol rx on tx off
>(conf-if-fo-0/12) mtu 9252 (packet size)
>(conf-if-fo-0/12) no shutdown (Enables the port)
>(conf-if-fo-0/12) show config
>exit (after enabling features for the port interface)

## Slide 10: Configure a range of Interfaces
You can configure multiple the ports using the interface range command
>(conf) interface range fortyGigE 0/16-80
>(conf-if-range-fo-0/16-80) show config
>(conf-if-range-fo-0/16-80) switchport
>(conf-if-range-fo-0/16-80) no ip address
>(conf-if-range-fo-0/16-80) spanning-tree rstp edge-port
>(conf-if-range-fo-0/16-80) flowcontrol rx on tx off
>(conf-if-range-fo-0/16-80) mtu 9252
>(conf-if-range-fo-0/16-80) no shutdown
>(conf-if-range-fo-0/16-80) show config

## Slide 11: Configure a port channel (lacp)
>(conf) interface port-channel 1 (id-number)
>(conf-if-po-1) no ip address
>(conf-if-po-1) switchport
>(conf-if-po-1) mtu 9252
>(conf-if-po-1) no shutdown
>(conf-if-po-1) show config (Shows the port channel setting)
To view the port channel’s status and channel members
># show interface port-channel 1 brief
Shows the port channel’s mode (L2 for Layer 2 and L3 for Layer 3 and L2L3 for a Layer 2-port channel assigned to a routed VLAN), the status, and the number of interfaces belonging to the port channel.
># show interface port-channel 1

## Slide 12: Configure an interface for lacp
LACP is configured by interface
Note: Minimum link (1) must be up for the port-channel
>(conf) interface range fortyGigE 0/0-8
>(conf-if-range-fo-0/0-8) no ip address
>(conf-if-range-fo-0/0-8) flowcontrol rx on tx off
>(conf-if-range-fo-0/0-8) mtu 9252
>(conf-if-range-fo-0/0-8) no shutdown
>(conf-if-range-fo-0/0-8) port-channel-protocol lacp
>(conf-if-range-fo-0/0-8) port-channel 1 mode active
Check the lacp link status
>do show interfaces port-channel 1
>do show lacp 1 (This gives link and member status)

## Slide 13: Configure a vlan
>(conf) interface vlan 2
>(conf-if-vl-3) name Service
>(conf-if-vl-3) description SE_Region
>(conf-if-vl-3) no shutdown
>(conf-if-vl-3) no ip address
>(conf-if-vl-3) untagged fortyGigE 0/12-80 (Adds the interface range 0/12-80 to vlan 2)
>(conf-if-vl-3) untagged port-channel 1 (Adds port-channel 1 to vlan 2)
>(conf-if-vl-3) show config
>(conf-if-vl-3) do show vlan
You can define IP network range for the vlan (If you have multiple vlan’s you’ll want to define a subnet as with GEO Lattus configurations)
>(conf-if-vl-2) ip address 10.10.10.1/24

## Slide 14: Configure a range of Interfaces
Lets configure additional ports using the interface range option and add them to vlan 2
>(conf) interface range fortyGigE 0/84-124
>(conf-if-range-fo- 0/84-124) show config
>(conf-if-range-fo- 0/84-124) switchport
>(conf-if-range-fo- 0/84-124) no ip address
>(conf-if-range-fo- 0/84-124) spanning-tree rstp edge-port
>(conf-if-range-fo- 0/84-124) flowcontrol rx on tx off
>(conf-if-range-fo- 0/84-124) mtu 9252
>(conf-if-range-fo- 0/84-124) no shutdown
>(conf-if-range-fo- 0/84-124) show config

## Slide 15: Changing a port assignment in a vlan
The addition ports we just configured default to vlan 1
Assign the ports to vlan 2
>(conf) interface vlan 2
>(conf-if-vl-2) untagged fortyGigE 0/84-124
>(conf-if-vl-2) do show vlan
To unassign a port from vlan 2
Note: If assigning multiple ports use the range option
>(conf) interface vlan 2
>(conf-if-vl-2) no untagged fortyGigE 0/12
>(conf-if-vl-2) do show vlan
Note port 0/12 is now in the default vlan 1

## Slide 16: Changing a port interface
I want to add port 0/12 that I previously configured in my interface range to my lacp port-channel 1
First I need to put port 0/12 back to its default settings.
Configure port to default:
>(conf) interface fortyGigE 0/12
>(conf-if-fo-0/12) show config
>(conf-if-fo-0/12) no mtu
>(conf-if-fo-0/12) no spanning-tree rstp edge-port
>(conf-if-fo-0/12) no flowcontrol rx on tx off
>(conf-if-fo-0/12) no switchport
>(conf-if-fo-0/12) shutdown
>(conf-if-fo-0/12) show config

## Slide 17: Continue
Now that the port is in default mode I can add it to my lacp port-channel 1
Add 0/12 port to lacp port-channel 1
>(conf) interface fortyGigE 0/12
>(conf-if- fo-0/12) no ip address
>(conf-if- fo-0/12) flowcontrol rx on tx off
>(conf-if- fo-0/12) mtu 9252
>(conf-if- fo-0/12) no shutdown
>(conf-if- fo-0/12) port-channel-protocol lacp
>(conf-if- fo-0/12) port-channel 1 mode active
Check the lacp link status
>do show interfaces port-channel 1 brief (Port status only)
>do show lacp 1 (This gives link and member status)

## Slide 18: Remove an interface from a port channel (lacp)
For a lacp port-channel
>(conf) interface fortyGigE 0/12
>(conf-if-fo-0/12) show config
>(conf-if-fo-0/12) no port-channel-protocol lacp
>do show interfaces port-channel
>do show lacp 1 (This gives link and member status)

## Slide 19: Changing a port assignment in a vlan
Remove a port from an existing vlan:
>(conf) interface vlan 2
>(conf-if-vl-2) no untagged fortyGigE 0/16
Move port to another vlan:
>(conf) interface vlan 3
>(conf-if-vl-3) untagged fortyGigE 0/16

## Slide 20: Saving switch configuration
Save your switch configuration changes
>copy running-config startup-config
Save your switch configuration to a USB drive.
Insert the USB drive: verify the USB drive is compatible and recognized by the Dell switch.
>show file-systems
Note the fields: Feature=FAT32 Type=USBFLASH and Prefixes=usbflash:
If the Feature is unknown you’ll need to format the USB drive.
>format usbflash:
To save the startup-config from the switch to the USB.
>copy flash://startup-config usbflash://startup-config_sw1

## Slide 21: Subnet Mask Cheat Sheet
 | Addresses | Hosts | Netmask | Amount of a Class C
/30 | 4 | 2 | 255.255.255.252 | 1/64
/29 | 8 | 6 | 255.255.255.248 | 1/32
/28 | 16 | 14 | 255.255.255.240 | 1/16
/27 | 32 | 30 | 255.255.255.224 | 1/8
/26 | 64 | 62 | 255.255.255.192 | 1/4
/25 | 128 | 126 | 255.255.255.128 | 1/2
/24 | 256 | 254 | 255.255.255.0 | 1
/23 | 512 | 510 | 255.255.254.0 | 2
/22 | 1024 | 1022 | 255.255.252.0 | 4
/21 | 2048 | 2046 | 255.255.248.0 | 8
/20 | 4096 | 4094 | 255.255.240.0 | 16
/19 | 8192 | 8190 | 255.255.224.0 | 32
/18 | 16384 | 16382 | 255.255.192.0 | 64
/17 | 32768 | 32766 | 255.255.128.0 | 128
/16 | 65536 | 65534 | 255.255.0.0 | 256