## Slide 1: StorNext 4.2 – EDLM with the Scalar i6k
Transfer of Information, Denver, CO, Sept 13-14, 2011
Eric Hawkins

## Slide 2: EDLM – What is it?
Extended Data Lifecycle Management
  Scalar i6000 based feature
    Scalar i500 will add feature in i8
  Provides Data Protection
    Tape Scanning
      Policy
      Manual
      RAS ticket notifications
    StorNext integration via SNAPI
      Suspect Count
      Issue Medcopy commands

## Slide 3: EDLM – What is it?
© 2011 Quantum Corporation. Company Confidential. Forward-looking information is based upon multiple assumptions and uncertainties, does not necessarily represent the company’s outlook and is for planning purposes only.
3
Notes: 3

## Slide 4: Scalar i6000 EDLM Configuration
© 2011 Quantum Corporation. Company Confidential. Forward-looking information is based upon multiple assumptions and uncertainties, does not necessarily represent the company’s outlook and is for planning purposes only.
4
Install EDLM drives
  HP LTO4 and LTO5 drives only
  Special flag on Sled to prevent usage in a customer partition
  Must be connected to dedicate 7404 IO Blade
Install EDLM license key
Create Library Managed Partition (LMP)
  Partition that is hidden from host applications
  Hosts the EDLM drives
Notes: 4

## Slide 5: Scalar i6000 Scanning
© 2011 Quantum Corporation. Company Confidential. Forward-looking information is based upon multiple assumptions and uncertainties, does not necessarily represent the company’s outlook and is for planning purposes only.
5
Manual
  Select individual tapes at any time
Policy
  One per partition
  Multiple options for each policy
Notes: 5

## Slide 6: Scalar i6000 Scan Policies
© 2011 Quantum Corporation. Company Confidential. Forward-looking information is based upon multiple assumptions and uncertainties, does not necessarily represent the company’s outlook and is for planning purposes only.
6
Enable External Application (StorNext)
  Library checks “suspect count” on dismount
  Scan performed if “suspect count” is set and above StorNext threshold
    Only scans it once at the threshold
    RAS Ticket generated on the library
  If scan fails “medcopy” is started
    Write protect the media on StorNext
    RAS Ticket generated on the library
Notes: 6

## Slide 7: Scalar i6000 Scan Policies (cont)
© 2011 Quantum Corporation. Company Confidential. Forward-looking information is based upon multiple assumptions and uncertainties, does not necessarily represent the company’s outlook and is for planning purposes only.
7
Tape Alert thresholds
  3 is the default but configurable
Time interval
  Day increments
  Be careful it’s possible to thrash the system
Scan on import
Notes: 7

## Slide 8: Scalar i6000 Scan Policy Types
© 2011 Quantum Corporation. Company Confidential. Forward-looking information is based upon multiple assumptions and uncertainties, does not necessarily represent the company’s outlook and is for planning purposes only.
8
Quick Scan
  Reads only cartridge memory (CM)
  Evaluates error counts and thresholds (not configurable)
  Less then one minute to scan
Normal Scan (default)
  Reads CM plus selected portions of the tape
  ~20 minutes to scan
Full Scan
  Reads CM and scans entire tape
  2 hours or more
Notes: 8

## Slide 9: Scalar i6000 Scan reports/results
© 2011 Quantum Corporation. Company Confidential. Forward-looking information is based upon multiple assumptions and uncertainties, does not necessarily represent the company’s outlook and is for planning purposes only.
9
Queued scans allow state changes
  Stop, Pause, Resume
Report details
  Individual media information
  Good, Bad, Suspect, Untested, Not Completed
Notes: 9