## Slide 1: StorNext 4.2 – File System Interfaces
Transfer of Information, Denver, CO, Sept 13-14, 2011

## Slide 2: What SNFS interfaces changed in 4.2
CvAPI_MoveRange
  New SNFS Client API
Windows OpenFileById Function support
  Provides mechanism for opening file by ID rather than name

## Slide 3: CvApi_MoveRange
This interface moves a range of file extents from a source file to a location in a target file
This API was requested by both Galaxy Development and by Bright Technologies
API files included with Full Storage Manager install on Linux platforms
Full description located in the SNFS API Guide
  Note: In an effort to start detaching the SNFS API from the SNAPI distribution, there is a separate SNFS API guide as part of the release of StorNext 4.2.

## Slide 4: CvApi_MoveRange Definition
int
CvApi_MoveRange(
int f_fd, /* Source File Descriptor */
uint64_t f_target_ino, /* Target File Inode Number */
uint64_t f_source_froffset, /* Source File Starting Offset */
uint64_t f_target_froffset, /* Target File Starting Offset */
uint64_t f_length, /* Data Size */
tmspec_t f_source_mtime, /* Source Expected mtime */
tmspec_t f_target_mtime, /* Target File Expected mtime */
uint32_t f_flags, /* Flags */
uint64_t *f_rsvd);

## Slide 5: CvApi_MoveRange Some Example Uses
Example #1 – Combining many sub-files into a larger file
  Use case: Ten 50 Megabyte data files are produced by separate processes. After processing completes the files will be concatenated in one large file
  Move all extents in file_a to offset 0 in target file
  Move all extents in file_b to offset 52,428,800 in target file
  Move all extents in file_c to offset 104,857,600 in target file
  And so forth…
  See the MOVE_APPEND flag in the SNFS API documentation for more info
Example #2 – Carve a source file into multiple target files
  Use case: One 500 Megabyte source file will be carved into 10 target files
  Move 52,428,800 bytes starting at offset 0 in target file to file_a
  Move 52,428,800 bytes starting at offset 52,428,800 in target file to file_b
  Move 52,428,800 bytes starting at offset 104,857,600 in target file to file_c
  And so forth…

## Slide 6: Windows OpenFileById
Support for the Windows OpenFileById Function has been added to Windows SNFS clients
In addition, calling NtCreateFile with the FILE_OPEN_BY_FILE_ID option is supported
Information on OpenFileById and NtCreateFile calls can be found in MSDN documentation
This functionality depends on SNFS RPL (Reverse Path Lookup) being enabled on the file system
  If RPL is not enabled the OpenByFileId call will return STATUS_NOT_IMPLEMENTED
Support for OpenFileById was requested by Group Logic to support upcoming enhancements to their products
There are no configurable options for this feature. It is always present as of 4.2 (assuming RPL is enabled)

## Slide 7: How to Use OpenFileById (NtCreateFile)
The File ID field can be located using the NtQueryInformationFile call with the FileInternalInformation
  See MSDN documentation for details on this call
The previous query will return two 32-bit fields. The ID value is built from these fields
FileID = ((ULONGLONG)info.nFileIndexHigh << 32) |
((ULONGLONG)info.nFileIndexLow & 0xffffffff);
The FileID value is passed in as the name in the NtCreateFile call while the flags field for the call contains the FILE_OPEN_BY_FILE_ID flag
  Note: NtCreateFile in this case is not creating a file but rather opening a file. (NtCreateFile is the swiss army knife of Windows calls)

## Slide 8: That’s all folks
Questions?