## Slide 1
Confidential - Do not distribute 1
INFINIDAT Backup Appliance Deep Dive - 9/17

## Slide 2: Agenda
B4260 Architecture Intro
INFINIDAT Backup Appliance (IBA) Specs
IBA Storage Architecture
Demo
Q&A

## Slide 3: What is it?
It is an INFINIDAT Model B4260
A Flash Optimized Purpose Built Backup Appliance
2 Active Deduplication Engines for 1PB – Physical Useable Capacity
  Racked and Ready Engine HA (Built-in)
  Internal racked FC & Ethernet Switch between iBox & DDE’s
  Use Market Proven, Licensed, Effective Variable Block Deduplication
Fully Racked & Wired with a simple custom Patch-Panel
Fully INFINIDAT Assembled, Installed, Configured & Supported
The INFINIDAT Backup Appliance (“The IBA”)

## Slide 4: IBA Naming Conventions
IBA model number B4260
  The B refers to an IBA solution (B for Backup)
    Added components - 3 x DDEs, FC-SW’s , ETH-SW
  The 4 refers to an F4000 or 4 enclosures
  The 2 means 2nd generation node (R730xd)
  The 6 refers to using 6TB HDD disks

## Slide 5: IBA Data Protection Portfolio
1-0, 1-1 or 1-2 & N-1
Site Replication
Limitations Up-to:
Upto ~76TB/Hr
128 VTL Partitions
1024 Virtual Tape Drives
18,000 Tape Media
256 NAS & Application Shares (NFSv3, SMB3, Application)
Upto ~ 200 Media Servers
Replication – 1-0, 1-1, 1-2, N-1
Pipes:
6 x 16GbE FC Ports (VTL)
- 4 Active
+ 12 x 10GbE Ports
- 8 Active
Or
18 x 10GbE Ports (no VTL)
- 12 Active

## Slide 6: Goals
Turnkey Solution to Enter Enterprise Backup Market
  Backup software independent – “Plugin and Play” for NBU, TSM, CV, Oracle, Veeam etc
  Integrating the best and proven technologies for the backup market
  Lowest Cost without compromise of Performance, Capacity or Quality
  Simplified, integration and enhanced solution under single vendor support
Support Enterprise Data Protection Ecosystems
  Go beyond the simple B2D use cases, software driven architecture or simple customers
  Enterprise scale in capacity and performance
GA Date
  Targeting September 29, 2017 (*=Post GA state of direction)
Notes: 1GB/s backend TP at peak time

## Slide 7: Deep Dive on the Architecture

## Slide 8: A look at the Hardware
Off the Shelf Hardware
Carefully selected based on performance, reliability, availability and cost
Assembled for highest performance & reliability
For optimized integration of exceptional Software based storage solutions by INFINIDAT

## Slide 9: Hardware Layout |DDE Node PCI cards
Common Dell Servers Improves Inventory, Stock, Support Simplicity
Slots 2 & 3 Qlogic 2662 16Gb FC internal connections to IBox
Slots 4, 5, 7 Used for customer connections
  Options of the following
    Intel X520 Dual Port 10Gb (NAS, OST, Replication)
    Qlogic 2662 16Gb FC (VTL) – Soft Zoning is preferred for FC – for proper Node Failover
      ZONE All Media Server Switch Ports to All DDE FC Switch Ports
    Typically Requested - 4 x 10GbE plus 2 x 16Gb/8Gb FC (for VTL integration)
    Optionally – 6 x 10GbE (when no VTL is required)

## Slide 10: Power Distribution
Each IBA Component has two PSUs
  (except internal 1Gb Switch)
Support for both single & three phase power
  single phase - 2 PDU per side
  three phase - 1 PDU per side
    * Customer Choice
If 1GbE Switch is down, only access to management is lost. All configured functionality continues to be served until Support can restore the switch.

## Slide 11: Internal Network Connectivity - Cabling
Optimized Switch Wiring
Patch Panel shows mgmt cable ports on IBA-Patch Panel but these are NOT for customer use
DDEs are managed through the IBA GUI
Support is managed thru iBox SA
iBox Patch Panel – Shelf Top = 4 x 1GbE
Customer Run Cables – UI & Support
IBA Patch Panel – Shelf Center
Top Row = 6 x 8/16Gb FC or 6 x 10GbE – Customer Choice
Bottom Row = 12 x 10GbE
Customer Run Cables – UI & Support
2 IBA Patch Panels for External Cabling
Minimal Customer Wiring
4 x 1GbE
12 x 10GbE
6 x 8/16Gb FC (VTL Only)
FC or 10GbE
FC or 10GbE
FC or 10GbE
4 x 10GbE
4 x 10GbE
4 x 10GbE

## Slide 12
DDE1
1
2
3
4
2
1
1
1
10GbE ports
16Gb FC ports
1GbE Mgnt port
Internal
Internal iDRAC
DDE2
1
2
3
4
2
1
1
1
10GbE ports
16Gb FC ports
1GbE Mgnt port
Internal
Internal iDRAC
DDE3
1
2
3
4
2
1
1
1
10GbE ports
16Gb FC ports
1GbE Mgnt port
Internal
Internal iDRAC
10GbE Network WAN
To Backup Media Servers & IBA Targets
FC Switch 1
FC Switch 2
VTL Rich Environment
10GbE is used for Replication
Each DDE FC Target Port is Zoned
To each Media Server Initiator Port
- 4 x FC Ports / DDE
2 x 10GbE Ports / DDE (Copper/Optical)
64Gb FC / DDE = ~ (6.4GB/Sec)
20Gb Ethernet / DDE = ~ 2.4GB/Sec
  Total Pipe BW / DDE = ~ 8.6GB/Sec
Optional Networking Schemes
Backup Media Server Initiator Ports
NOTE:
1GB/Sec = 3.6TB/Hr
30.9TB / Hr / DDE

## Slide 13
DDE1
1
2
3
4
6
5
1
1
10GbE ports
1GbE Mgnt port
Internal
Internal iDRAC
DDE2
1
2
3
4
6
5
1
1
10GbE ports
1GbE Mgnt port
Internal
Internal iDRAC
DDE3
1
2
3
4
6
5
1
1
10GbE ports
1GbE Mgnt port
Internal
Internal iDRAC
10GbE Network WAN
To Backup Media Servers & IBA Targets
Ethernet Rich Environment- No VTL
(OST/NFS/CIFS & Replication)
10GbE is used for Data & Replication
6 x 10GbE Ports / DDE (Copper/Optical)
60Gb Ethernet / DDE = ~ 7.2GB/Sec
  Total Pipe BW / DDE = ~ 7.2GB/Sec
Optional Networking Schemes
25.9TB / Hr / DDE
NOTE:
1GB/Sec = 3.6TB/Hr

## Slide 14
DDE1
1
2
1
2
4
3
1
1
10GbE ports
16Gb FC ports
1GbE Mgnt port
Internal
Internal iDRAC
DDE2
1
2
1
2
4
3
1
1
10GbE ports
16Gb FC ports
1GbE Mgnt port
Internal
Internal iDRAC
DDE3
1
2
1
2
4
3
1
1
10GbE ports
16Gb FC ports
1GbE Mgnt port
Internal
Internal iDRAC
10GbE Network WAN
To Backup Media Servers & IBA Targets
FC Switch 1
FC Switch 2
Balanced Mix
Ethernet & VTL Rich Environment
10GbE is used for Data & Replication
VTL Used for Data Only
Each DDE FC Target Port is Zoned
To each Media Server Initiator Port
- 2 x FC Ports / DDE
2 x 10GbE Ports / DDE (Copper/Optical)
32Gb FC / DDE = ~ (3.2GB/Sec)
40Gb Ethernet / DDE = ~ 4.8GB/Sec
  Total Pipe BW / DDE = ~ 8GB/Sec
Optional Networking Schemes
NOTE:
1GB/Sec = 3.6TB/Hr
28.8TB / Hr / DDE
Backup Media Server Initiator Ports

## Slide 15
Ideally Workloads are balanced between DDE’s
Backup Server
Backup Server
Backup Server
Backup Server
Backup Server
Backup Server
Oracle Server
Oracle Server
INFINIDAT
B4260
DDE1
DDE2
Balance work across both DDE’s
Keep Similar Workloads Together for Higher Efficacy
Balance us of IP’s and FC Ports on Each DDE
Balance use of VTL, NFS, CIFS
Use OST plugin wherever Possible (NetBoost/ACCENT)
For Best Results
VM Workloads
Windows Workloads
UNIX Workloads
Oracle Workloads
Global Dedupe
is
DDE Centric
@ 506TB/DDE
The DDE’s are simply Disk Targets for Strategic Backup Data & Network Reduction

## Slide 16
Oracle
Replication
Scenario 2
RMAN Scripts point backups to IBA “SBT_Tape” Devices on both IBA’s (DUPLEX) allowing immediate access to restore from either target.
Oracle Workloads are balanced between DDE’s
Oracle Server
Oracle
Server
Oracle
Server
Oracle
Server
Oracle Server
Oracle Server
Oracle Server
Oracle Server
INFINIDAT
B4260
DDE1
DDE2
Balance work across both DDE’s
Keep Similar DB Workloads Together for Highest Efficacy
Balance us of IP’s and FC Ports on Each DDE
Balance use of “Application Shares” or NFSv3 targets
Use Oracle plugin wherever Possible (NetBoost/ACCENT)
For Best Results
UNIX Workloads
Oracle Workloads
The DDE’s support simple Disk Based Targets for Strategic Backup Data & Network Reduction
UNIX Workloads
Oracle Workloads
Special Oracle Application Shares
For Disk & Network reduction in Backup
Up-to 76TB/Hr
Backup & Restore
Oracle
Replication
Scenario 1
RMAN Scripts point backups to IBA SBT_Tape Devices then the IBA replicates the data.
Extreme Performance & Reliability at the Lowest Possible Transferable
$ Cost/TB in its Scale.

## Slide 17: Networking the DDE’s
NIC Bonding with LACP provide the highest Network Reliability & BW to IP targets – Mode 0 (Active/Active)
Using all 10GbE NICs is recommended
Allowing Data & Replication from the IPs can also make best use of all networks
When all clients can use Jumbo Frames set MTU to 9000
IP addresses are used for OST integration, RMAN backups, NAS and Application Shares, and Veeam container Integrations. Bigger pipes = bigger yields
4 active 10GbE ports on each DDE provide 40Gb performance for physical data transfer or ~ 4GB/Sec/DDE to IP targets
2x16Gb FC ports (for VTL) will provide approximately 3.2GB/Sec to DDE VTL targets.

## Slide 18: IBA Installation
IBA installation will need the standard IBOX requirements (plus) (Drives installed and FW update on Delivery – System installed in ~ 4hrs)
4 x 1Gb ethernet connections (mgmt per node + SA)
5 IP addresses (1 per node + 1 float + SA)
IBA DDE’s Require FC & 10GbE connections
12 x 10GbE (LACP or Independent IPs for Data & Replication)
6 x 8/16GbE FC (VTL only)
The install process will be to install the InfiniBox per normal procedure and then the IBA pieces after
Notes: This is all the connectivity that we (Infinidat) need for the install - the customer will still need 10Gb copper/fiber or FC connectivity for data/replication traffic

## Slide 19: Internal FC Connectivity & Cabling
ALL INFINIDAT MANAGED
DDEs have 2 connections per internal FC switch
Each IBox node has 2 connections per internal FC switch
Total of 12 FC ports used per internal FC switch
FC switches are internal ALL INFINIDAT MANAGED!
FC internal Switches are used for iBox to DDE volumes!
* This is Not used for VTL services on the DDE.
All Pools & Volumes are Pre-configured, Zoned, & Mapped

## Slide 20: All Storage is Pre-Configured DDE’s use a Boot from SAN model for Highest Performance & Reliability All Storage to Each Deduplication Engine is managed in Separate Protected Pools All Volumes are pre-configured and Mapped to Each DDE Customers are not responsible for Storage Management of the IBA HW or SW Customers are not responsible for HW component Replacement (internals) Single-Sign On UI (Very INFINIDAT friendly) Integration with InfiniMetrics
Notes On Storage Integrations
DDE Volume Configuration
    Block size - 4K page size
    Thick Provisioned
    Compression - IBox compression Off - Compression done in DDE software for dedupe LUNs
    Pool Buffer is set to Unlimited
    Alerts Warn - 80% Critical - 90% ( Warnings may warrant Old Backup Expiration )

## Slide 21: Shutdown process
Customers will need to contact support for graceful shutdown of the IBA system at GA
To shutdown the system support will need to 1st shutdown each DDE and then the InfiniBox
DDE reboots and Hot Spare Node Replacements
– Take approximately 15 minutes on GA

## Slide 22: IBA - 12 month roadmap
Full HA for DDEs
Mix-Mode & Gateway-mode
  use the underplaying IBOX for replication, emergency restore and secondary storage
  Add DDEs to existing customer’s IBOX
IBA based on F2280
IBA B4K using 10TB Drives
1PB DDE capacity
50%+ DDE performance increase
Infinimetrics to monitor DDEs performance
IBA replication to Leitrem cloud
Accent (source dedupe) to support more platform

## Slide 23
Questions?