## Slide 1: Scalar LTFS 2.0 - TOI
Eric Hawkins
4/3/13

## Slide 2: Intro
2012 Quantum Corporation. Company Confidental
2
Changes from 1.0 to 2.0
  Moved to Dell 520
  LTO6 support
  IBM drive support
Installation and Setup
  Setup Wizard (all the Configuration menus; run only on initial login)
  License key might be an issue during setup
    Generated on the Quantum website by the customer
    Customer shipped a License Key Certificate
Operations
  Format/Attach/Sequester media
    Media have to be attached to be available for use
  How to map via NFS and CIFS/Samba

## Slide 3: LTFS tape contents
2 partition tape
  1st partition contains the file mapping structure (index) of the media
  2nd partition contains the data
Index
  XML file that contains…
    details of the file locations on the media
    Metadata
  Written to the media itself (self describing)
Extents
  Contained in the index
  Identifies file segments and tape location
  Single file can be 1 to 1000’s of Extents
    Depends on filesize and protocol
    CIFS - usually one
    NFS - dependent on mount options and usage model

## Slide 4: Best Practices
Reference Chapter 2 of User Guide (Best Practices Guide)
  6-67514-01
  “Must reading”

## Slide 5: Key Best Practices
NFS on Linux
  Use nfs version 4 (not 3)
  1MB rsize/wsize
    Lower sizes cause high number of extents (large index files)
  Use directio via the “dd” command
    Out of order extents without directio (causes slow read performance)
File Browsers tend to want to reload all files to get thumbnails
One drive per user (best possible usage model)
  Drive over subscription
    CIFS: Network busy error and must retry
    NFS: Based on otime (mount param) can timeout as well, must retry
Known good tape
  Customer writes non-critical data to a tape that will only be used to verify possible drive failures.

## Slide 6: Key Best Practices (cont)
2012 Quantum Corporation. Company Confidental
6
Library must be partitioned with LTO5 and LTO6 in different partitions
Avoid editing files on filesystem
  some editors generate temp files which have to be written to media
Deleting files from the filesystem does not free up space
  Format is only way to reclaim space, however data is not recoverable after a format.
Import/Export operations can cause partition to go offline

## Slide 7: Tools
2012 Quantum Corporation. Company Confidental
7
Save/Restore
  Save current config and allows restore
  Must be at the same version of software to restore as the save was taken
  Saves a maximum of 1GB (uncompressed) of index files most recently used
    Will not save index file for currently mounted tapes
  Must have the matching Quantum serial number to restore if appliance was replaced.
    Use service.sh to set this
Capture snapshot
  “normal snapshot” – keep it to ~10MB or less to email it
  “extended snapshot” – gets all sltfs logs and cores. Can be gigabytes.
  “component log collection” – dell collect

## Slide 8: Tools (cont)
2012 Quantum Corporation. Company Confidental
8
Security
  IP list only (no ranges)
  Customer will be very interested in this
Update firmware
  Not allowed if tapes are mounted or any tickets are open
  Normally takes 10-15 minutes
  If component firmware upgrades required can take an hour
Diagnostic tickets
  3 Levels
    Low – Blue; Medium – Yellow; Red - High
  Always check the library for tickets
    Specifically for Tape alerts on drive and media
  Each ticket has resolutions to follow
    If-then structure
    Find changes or helpful items

## Slide 9: Items to be aware of
2012 Quantum Corporation. Company Confidental
9
SLTFSCK
  Recovery of media by the user to a valid index
    If power outage during write and index is not written
    Will drop data up to the last written index.
  Currently not functional in 2.0 (will be fixed in 2.1)
    TSB likely in case service becomes involved
Library and drive reservations
  Crash of SLTFS can leave reservations on drive and library
  Restart should release reservations
  Re-cabling HBA or switching SLTFS appliances may not release them
  Reboot drive and/or library (look for tickets on library)

## Slide 10: Troubleshooting
2012 Quantum Corporation. Company Confidental
10
Snapshot Logs
  /scratch/collect/node1-collection
    Collect.txt – system information
      Platform details/core backtraces/scsi info/network details
    Altfs-info directory (sltfs specific logs)
      Depending on the usage these logs can be rolled every 10 minutes
      Altfs.log* – contains all sltfs logs
        Search for ERR can give you a feel for an error that occurred
      Altfs_debug.log* - debug level logs (development only)
      Altfs_ltfs.log* - drive communications via ltfs
      Altfs_uti.log – uti utility logs (development only)
      Altfsdb.log – altfs database dump
      Configchanges.log – configuration changes that happened via the gui
      Directory.log – list of sltfs owned directories
      Driveusage.log – list of drive mount and dismounts
      Fileops.log* - list of filesystem operations received from host
      Gui.log – activities from the gui

## Slide 11: Troubleshooting (cont)
2012 Quantum Corporation. Company Confidental
11
Snapshot Logs (cont)
  /scratch/collect/node1-collection
    Altfs-info directory (sltfs specific logs)
      Memcheck.log – 5 minute memory tracing
      Memory.log – memory at time of snapshot
      Php_error.log – php (used by the gui) errors
      sltfsWS.log – Webservice logging (possible external apps can use WS)
      Vdbdb.log – RAS database dump
        sl_event_details have tickets
        DT_BAD tickets visable as well, these are not customer facing

## Slide 12: Troubleshooting (cont)
2012 Quantum Corporation. Company Confidental
12
Darryl Torske - Engineering contact
DT054 – Unexpected System Restart
  Collect Extended snapshot
  System likely panic’d or sltfs cored
  Contact Darryl with this information
  Will see DT055 – Forced unload for each mounted volume

## Slide 13: Questions
2012 Quantum Corporation. Company Confidental
13
Q and A