## Slide 1
July 9th, 2015
UI Demo & Best Practices

## Slide 2: Agenda
Product Demonstration
  Install licenses
  Virtualized RAID Overview
  Creating LUNS
  Mapping Hosts
  Traditional RAID (short review)
  IO demonstration
  Configuring Users
  Configuring Email/SNMP
One-off Tasks
  Rebooting
  Firmware Updates
  Logs
Best Practices
Q/A

## Slide 3: QXS & Dot Hill differences

## Slide 4: Traditional RAID (Linear)
SSD
SSD
7K
7K
10K
10K
Disks
Pool
Linear LUNs
LUN
LUN
LUN
LUN
LUN
LUN
RAID10
RAID6
RAID1
RAID Sets
Notes: QXS uses linear RAID; LUNS are served by a single, dedicated RAID set
NOTE: The Dot Hill branded controllers can also do linear, but it’s no longer the norm.

## Slide 5: Virtualized RAID
Virtual LUNs
LUN
LUN
LUN
LUN
LUN
LUN
SSD
SSD
10K
10K
7K
7K
Disks
RAID Sets
RAID6
RAID1
RAID10
Pool
Pool
Notes: Dot Hill branded array are typically configured with virtualized RAID.
NOTE: Dot Hill branded arrays can also do linear, but most of the time, the end customers will want virtualized RAID.

## Slide 6: Virtualized RAID
Virtualized RAID Is:
Virtualized Storage via Pools
Distributed across multiple RAID sets
Providing:
Algorithms that monitor I/O access patterns…
…to automatically cache data or move it to optimal locations based on workload.
Using 4MB pages
Auto Tiering
Plus Intelligence:
Quick Rebuild
Space allocation on demand
Advanced Copy Services
RealStor 2.0

## Slide 7: Licensing

## Slide 8: Licensing for RealStor 2.0
Included in the box:
  Tiering for HDD’s
  Thin Provisioning
  Rapid Rebuild
  Virtualized Snapshots
  SSD Read Cache
Licensable Options
  Tiering for Flash
Software support
  One year of software support is required with this feature
Associated Hardware
  4004 series arrays
  3004 – coming in Q3
  6004 – coming in Q4

## Slide 9
GUI Demonstration

## Slide 10: Best Practices
Virtual Volumes- Balance

## Slide 11: Balance across controllers
Strive for a workload balanced across controllers/pools
  Unbalanced pools are more difficult to expand
  long-term, one controller could end up being a bottleneck after expansion

## Slide 12: Balance Among disk groups
Disk count balance
RAID Balance
Tier is as slow as the slowest disk group
Strive for common rotational latencies in a tier (all 10K or all 15K)
dgA02 RAID 5
dgA03 RAID 5
dgA01 RAID 1
Pool A
dgB02 RAID 5
dgB03 RAID 5
dgB01 RAID 1
Pool B

## Slide 13: Disk Group Count
Write Queue-depth per disk group is 100
Latency sensitive, high IOPS applications could hit this queue depth
dgA02 RAID 5
dgA01 RAID 10
Example 1: Same count, but less q-depth
dgB03 RAID 5
dgB04 RAID 5
dgB01 RAID 1
Example 2: Lower capacity, but higher q-depth
dgB02 RAID 1

## Slide 14: Balance disk groups across drawers (4U56)
Each controller is limited to 4 lanes of SAS to each drawer.
  Limits throughput to 2.1 GB/sec into each drawer
If you put an entire disk group in one drawer, then the single drawer becomes a bottleneck
Best Practice: Spread disk groups across the drawers for maximum throughput

## Slide 15: Best Practices
Virtual Volumes & Parity Based RAID

## Slide 16: Key Concept Reminder
4MB “pages” of data are building blocks
Large impact to RAID5/RAID6 disk groups
  RAID5/RAID 6 use 512K chunk size if the # of data disk is a power of 2
  RAID5/RAID6 use a 64K chunk size if the # of data data disk is not a power of 2
  Sequential workloads can be impacted by non-aligned writes
Virtual LUNs
LUN
LUN
LUN
LUN
LUN
LUN
Disks
Disk Group
7K
7K
RAID6
SSD
SSD
RAID1
Pool
Pool

## Slide 17: Unaligned Write example
Disk 1
Disk 2
Disk 3
Disk 4
Disk 6
A1
A2
A3
A4
A5
B1
B2
B3
B4
B5
RAID5 (5+1): Stripe Unit=512K, Stripe size=2MB
Stripe A
Stripe B
A single page doesn’t align.
The data from disk 5 and 6 must be read so that parity can be re-calculated. Extraneous writes for every page written
Disk 5
Ap
Bp
14 Disk I/Os + 1 XOR to write a single page
1 page written with 1 Full Stripe Writes, and 1 partial stripe write
NOTE: The array will set the stripe unit to 64K to mitigate this issue

## Slide 18: 4MB page aligned writes
Disk 1
Disk 2
Disk 3
Disk 4
Disk5
A1
A2
A3
A4
Ap
B1
Bp
B2
B3
B4
RAID5 (4+1): Stripe Unit=512K, Stripe size=2MB
Stripe A
Stripe B
1 pages written with 2 Full Stripe Writes – the Holy Grail!
10 Disk IO’s & 2 XOR calculations

## Slide 19: Best Practices
Best Practices – Others

## Slide 20: VMWare
When volumes are removed from an ESX host without properly un-mounting, then the ESX host will query the storage system for the LUN
The array returns “Not Ready”; ESX keeps trying!
This will slow down the host
Use the following CLI command:
# set advanced-settings missing-lun-response illegal

## Slide 21: Q/A

## Slide 22: RAID5/6 & Virtual Volumes
Partial-stripe writes severely degrade performance
To keep performance high, data drives should be a power of 2:
  RAID6:
    2 data drives + 2 for parity
    4 data drives + 2 for parity
    8 data drives + 2 for parity
  RAID5:
    2 data drives + 1 for parity
    4 data drives + 1 for parity
    8 data drives + 1 for parity
Consider linear volumes unless you want quicker rebuild

## Slide 23: Tiering data placement
Initial writes
  Random – highest tier
  Sequential – highest HDD tier
SSD
SSD
10K SAS
10K SAS
NLN
NLN
SSD
SSD
HDD
HDD
10K SAS
10K SAS
NLN
NLN
SEQ
RAND
SEQ
RAND
SEQ
RAND

## Slide 24: Data Placement Considerations
SSDs will not be used for large block sequential I/O
Archive tier not used until Standard tier is 95% full:
  3-tiers should be rare
  Use 3-tiers only when you must have faster-spinning disk for performance AND you can’t reach capacity goals without the slower disk
  2-tiers can meet almost all needs

## Slide 25: Automated Tiered Storage (RealTierTM)

## Slide 26: Real-Time Tiering
Real-Time analysis and data movement
  Continuous monitoring and adjustment
Autonomic
  Runs automatically in the background without any user intervention
Fine-grained data movement
  “Sub-LUN” tiering
  4MB pages of data
SSD
Fast HDD
Nearline HDD

## Slide 27: Tiering
What this means:
  Constant background scanning for hot data
  Hot pages are moved immediately – no waiting
  Performance improvements can be seen almost immediately.
Shows immediate performance gains with difficult (cache-unfriendly) workloads
Optimized to move data up
Excellent for Database & OLTP workloads
Hot Data
Cool Data
Cold Data

## Slide 28: Thin Provisioning (RealThinTM)

## Slide 29: Thin Provisioning
Enabled/Disabled for all volumes in a pool
Disk space is used only when it is written to
  No space reservations are made at LUN creation time
LUN size is independent of physical disk space
Add capacity when needed
Reclaim unused space
  T-10 Unmap
  Background space reclamation
Used space
Free space
Pool
Notes: RealThin allows users to provision volume sizes independently of physical storage and thus allows you to buy only what you need up front. And we provide a robust set of alerts to ensure proper notifications as you approach the provisioned limits.

## Slide 30: Thin Provisioning
Alerts sent at configurable capacity thresholds
Low Threshold
  25% of space consumed
Mid Threshold
  50% of space consumed
High Threshold
  Calculated (approximately 90-95%)
  Not user configurable
What happens when we run out of space?
  If we’re ‘overbooked’ and exceed the high threshold then we switch to write-through mode
  Lowers performance, but gives more time to add storage

## Slide 31: Rapid Rebuilds (RealQuickTM)

## Slide 32: Quick Rebuild
Affected stripes
Rebuilt user data
Disk 1
Disk 2
Disk 3
Notes: RealQuick is Dot Hill’s Rapid Rebuild feature. Since we have knowledge of the usage of the pages of a failed drive, we can now rebuild only the data that you are using – not the full RAID set configured on the disk. Typically, we have found that this can improve the performance of standard rebuilds by at least two to five times. There is nothing to set or configure. This substantially narrows the window of vulnerability that occurs when a large capacity disk drive fails.

## Slide 33: Quick Rebuild
Advantages:
  LUNs are spread across many RAID sets. So one RAID set rebuilding only affects a fraction of all disk I/Os
  Less rebuild work to do – so affected disks can return to full performance quickly.
  Volumes become fault tolerant more quickly – user data is restored to full protection more quickly.
  Speedup is directly proportional to amount of unused disk space
When is this important?
  When using large capacity drives 4TB/6TB/8TB drives
  When using parity-based RAID in disk groups (RAID5, RAID6)

## Slide 34: SSD Read Cache (RealCacheTM)

## Slide 35: SSD Read Cache
Improves performance of read-centric transactional workloads
The SSD cache becomes an extension of the controller cache
A lower cost way to get performance improvement from SSD
  Uses ½ the number of SSDs as the SSD tier
  Holds a (volatile) copy of data
  Read cache SSD failure never causes data loss
  Provides improved performance in random, read-centric workloads
11/14/2013
Controller Cache
Virtualized
Backend
I/O Mapping
HDDs
I/O
Hints
Copy Data
SSD
Notes: How it works
  Similar to tiering: based on combined LRU/LFU algorithm…
  …except that it takes “hints” from the controller cache about pages which it would like to keep in cache, but can’t
  Also, pages with heavy write activity as considered less important than read-centric pages
  Hot pages are copied (rather than moved) to SSD
  Reads are satisfied from SSD. Writes go to both SSD and HDD
RFC Discards
  If read cache is full, we have to discard
  We discard the lowest ranked page, except there’s hysteresis: pages already in cache get a slight boost in rank to lessen churn

## Slide 36: Virtualized Snapshots (RealSnapTM)

## Slide 37: Virtualized Snapshot
  All volumes are equivalent:
    All volumes are snappable, including snapshots
    No loss of performance for snaps
    Opens new opportunities for using snaps (e.g. data mining, daily backups)
  High Performance
    Write Redirect uses less I/O operations than COW
    All volumes have the same high performance; even the 100th snap of a volume
    Leverages larger controller CPU memory
Volume
Source Volume
Take Snapshot
Page
Tables
Snapshot Volume
Volume
Page
Tables
Page
Ref=1
Page
Ref=1
Page
Ref=1
Page
Ref=2
Page
Ref=2
Page
Ref=2
Notes: How is a snapshot taken?
    A snapshot is a new volume with identical data to the original
    To do this, we simply create a new volume and create PS page tables that duplicate the originals
    We also need a new data structure to keep track of multiple references to the same physical page. This new data structure is the Reference Count Table

## Slide 38: Large LUNs

## Slide 39: Large, Flexible Volumes
Volume sizes up to 128TiB (140TB)
  Spanning up to 256 HDDs (architectural limit)
Seamless capacity expansion
  Data automatically rebalances to newly added RAID sets
  IOPS & Throughput scale with additional storage
  Volumes can be expanded