## Slide 1
Brian Raccuglia
Entry Xcellis Workflow Director

## Slide 2: Entry Level XWD
Single Xcellis Workflow Director server node and QXS3/4 arrays (R630 server)
Uses the same server, networking options and storage options (QXS3 and QXS4) as the Dual node Xcellis
CentOS 7.3 based installation like dual node XWD
Optional expansion node available for single node installations
Configured as a single XWD HA node with a cluster of 1 node
  Required for ease of integration of a second node and access to the standard HA shared filesystem mount point
Uses standard Xcellis install menu option
New service menu conversion option “Make Single Node” to be run at customer install time to convert the node to a “single” node installation
  Makes the node “node 2”
  Sets the expected node count to 1 so the GUI does not expect to find a second node

## Slide 3: Entry Level XWD
New service menu option to add a second node
  “Make Dual Node” option available in the Conversions menu to convert a single node installation back to a dual node installation.
Node 2 services like DAE and Connect are supported and functional on a single node configuration
Connect install supported

## Slide 4: Second Node Expansion
Available for Entry XWD and Artico single node installs
New node must have same hardware and software configuration
  If new node is shipped with the latest factory code release, the installed node will need to upgrade to the current shipping code before expansion is done
New expansion node will become “node 1” since that is the default at install from the factory for a node
Existing node 2 node will need to have the “Make Dual Node” service option run to enable the addition of the second node
  This activates the GUI and allows configuration of a secondary node

## Slide 5: Second Node Expansion
No Connect install support for expansion node
Steps to add second node
  Set system serial number to match existing node using the service menu (Serial Numbers -> Set All Numbers)
  Configure initial network configuration so the GUI on the existing node 2 can access the new node over the network
  Cable network and storage connections to the shared QXS array
  On existing node 2, run the “Make Dual Node” option from the Conversions menu in the service menu (More Tools -> Engineering Tools -> Conversions Menu -> Make Dual Node)
  Go to the StorNext GUI “System” page and scan for the new secondary node, configure additional network settings if applicable and configure the time/date
    Both nodes will reboot when applied. This is a limitation in 6.0.0. Future releases will only reboot the new node to apply the settings so no downtime is required

## Slide 6: Second Node Expansion
  Add the new node IP to the FS Nameservers configuration using the GUI
  Attempt to perform the HA conversion on the new node which will prompt for the licenses to be installed for the new node
  Install updated license.dat file that includes licenses for both nodes
  Perform the HA conversion of the new secondary node
  Perform manual failover to the new node 1 to optimize performance and services
No visible difference between an expanded XWD and a fresh installed dual node XWD system
  Service menu logs will be the only way to tell that a system was expanded with a second node without going to the IB records