## Slide 1
Brian Raccuglia
Artico Changes

## Slide 2: Artico Changes
Based on current Xcellis Workflow Director platform ( 1U R630 server)
CentOS 7.3 based installation like XWD
Single or dual node factory options available
Optional expansion node available for single node installations
95% equivalent to the Xcellis Workflow Director with the exception of the following
  System serial number contains product code “CKG” instead of “CKH”
  StorNext GUI will display “Artico”
  Disk expansion options are the same as previous Artico, RBOD plus one optional JBOD
  RAID layout/luns is the same as original Artico
  Front panel LCD will display “Artico” instead of “Xcellis”
New fresh install option “Artico” on ISO install

## Slide 3: Artico Hardware Changes
Only the QXS312 (2U12) array is supported.
QXS-3 Array connection is iSCSI.
Up to two QXS312 chassis (RBOD and JBOD)
Supports 4TB, 6TB and 8TB drive capacities.
A minimum of one Client add in card must be selected from:
  Dual port 10G base T
  Dual port 10G SFP
  Quad port 1G base T
Optionally a second Client add in card can be selected from the above list or a Quad port 16G FC HBA.