## Slide 1
Brian Raccuglia
Xcellis Workflow Extender (XWE)

## Slide 2: Xcellis Workflow Extender
Uses a single instance of the same R630 server used on Xcellis.
Connectivity options
  Dual port 10GbE SFP - Dual port 16b FC
  Dual port 10G base T - Quad port 16Gb FC
  Dual port 40GbE - Dual port 32Gb FC
  Quad port 1G base T
CentOS 7.3 based installation like XWD
Replacement for G300 gateway
Minor service menu network changes added to allow more flexibility with port configuration

## Slide 3: Service Network Menu Change: Default Gateway
For XWE gateways, Xcellis and G300R based, Default Gateway assignment is done as part of an interface configuration (no longer as part of host configuration).
This change is to ensure a default gateway is assigned to the system that is accessible from one of the system configured interfaces. (Bug 66445, missing default route)
Configure host setting no longer includes default gateway setting:
  1) Configure host settings - Configure hostname, domainname, and DNS servers.

## Slide 4: Service Network Menu Change: Default Gateway
Default gateway is designated through one of the following interface configuration options:
  2) Configure Metadata Network - Configure metadata network settings.
  3) Configure Gateway Client Network - Configure Gateway client network settings.
  4) Configure/Unconfigure Interfaces - Configure/Unconfigure network interfaces.
For example during Gateway Client Network configuration, as following:
  bond1 slaves [eth1,eth4,eth5]: s
  IP address []: 10.2.2.124
  Netmask []: 255.255.255.0
  Gateway IP []: 10.2.2.1
  Make 10.2.2.1 the Default Gateway(y/n)?

## Slide 5: Service Network Menu Change: Default Gateway
Only will be asked this question if:
  The IP address and Gateway IP address for the interface being configured are different (indicating the provided Gateway IP address belongs to an external host)
  The default gateway is not assigned yet, or
  The Gateway IP address for the interface being configured is different than the already assigned default gateway.
Answer yes to this new question if
  No default gateway is yet assigned, and this is the default gateway you want to assign for the system, or
  if there’s a need to change the default gateway
Answer no to this new question in all other circumstances

## Slide 6: Service Network Menu Change (All systems): Bonding
Due to limitations in Mellanox implementation of Ethernet networking, bonding of 40GbE interfaces does not work properly, as a result:
40GbE interfaces not available for selection as slaves when creating a bond:
  4) Configure/Unconfigure Interfaces - Configure/Unconfigure network interfaces.
    0) Configure a bond - Configure a bond.
40GbE interfaces are still available in other individual interface configuration menu options:
  0) Display external ports - Display all external ethernet ports.
  4) Configure/Unconfigure Interfaces - Configure/Unconfigure network interfaces.
    1) Configure an interface - Configure an interface.
  5) Update an Interface - Update a bond's slaves,mode,mtu or an interface's mtu parameters.