## Slide 1
Configuration and Tuning
SNFS Development Team
7-March-2012

## Slide 2: Storage Tuning - Metadata
Metadata Storage
  Metadata workload consists of small, random I/O
    RAID 1 or RAID 10 recommended for metadata storage
  Journal consists of sequential read I/O during FS startup and sequential write during normal FS operation
  Write-behind caching recommended for both metadata and journal
    Write-behind cache requires battery backing for metadata and journal data

## Slide 3: Storage Tuning - Data
User Data Storage
  Storage tuning depends on usage
    RAID 5 or RAID 6 generally used for user data
    RAID Stripe Size should be tuned per the common I/Os in the File System’s workflow
  Choosing a RAID stripe size that is too large for a workflow can have negative impact on the performance of the file system
    Writes into the RAID that are not a full stripe in size will incur a read-modify-write penalty

## Slide 4: A note on RAID Read-Modify-Write
One key aspect to RAID performance tuning is preventing unnecessary I/Os from consuming the array’s throughput
There are special behaviors to keep in mind for RAID 5 and RAID 6 configurations
  These configurations stripe I/Os across multiple disks as well as save parity calculations for each stripe
In the event that a write to the array does not perfectly cover a stripe width, extra read I/Os are necessary to determine a stripe’s parity calculation
Reducing the instances of writes which do not cover a whole stripe will improve the overall throughput of the RAID device
For example, If most application I/Os are 256k in size, a RAID stripe size of 256k should perform better than a stripe size of 1m

## Slide 5: Other notes on RAID configuration
There is generally little advantage in configuring read-ahead settings for metadata disks
Write-behind caching generally shows a big win for metadata disks
  For metadata, battery backup is required for write-behind configurations
In workflows where RAID throughput should be optimized at the expense of resiliency, some customers have disabled cache mirroring between the two controllers in an array
  The two controllers in the array run independently serving separate LUNs
  Fault tolerance is degraded in this configuration, but performance is boosted

## Slide 6: Network Tuning - Metadata
SNFS best practices recommends a dedicated, switched, metadata network
  The latency of RPCs between SNFS clients and servers have a significant impact on SNFS metadata op rates
  Other network services will impact the SNFS metadata performance
    NFS/CIFS/iSCSI/etc. should not be run on the same network as the metadata traffic between client and server
Bonded or multi-homed MDCs are supported for additional fault tolerance

## Slide 7: SNFS Stripe Group Configuration
SNFS metadata and user data should be configured on different stripe groups
Multiple LUNs may or may-not be used in each stripe group
Stripe Breadth – this value indicates the amount of I/O performed on a LUN before submitting I/Os to the next LUN in the stripe group
In general, the Stripe Breadth value should match, or be a multiple of, the RAID stripe size
  Stripe Breadth values that are not tuned to the RAID stripe size will see a higher instance of read-modify-write in the array

## Slide 8: SNFS Global configuration
InodeCacheSize – Indicates the number of inodes that can be stored in the FSM cache
  Increasing this value can improve the inode lookup cache hit rate
  Cache hits can be determined through the qustat “ICa Hits” counter.
BufferCacheSize – This setting reflects the amount of memory available to cache metadata blocks
  Increasing this value can improve the block read cache hit rate
  Cache hits can be determined through the qustat “BufCa Hits” counter
ThreadPoolSize – This setting reflects the number of worker threads available to process client requests
  Values between 32 and 128 are common

## Slide 9: SNFS Global configuration
InodeStripeWidth – rotates a single file’s allocations across the data stripe groups
  can help reduce hot-spots on the file system if very large files are used.
AllocationSessionReservationSize – defines a session size when multiple files are created in the same directory

## Slide 10: Client Configuration
When tuning client configurations the following SNFS mount options should be considered (see mount_cvfs man page for more details)
  auto_dma_read_length/auto_dma_write_length - By default, all I/Os at this value or above will be direct, all I/O sizes below this value will go through the buffer cache. These values can be set independently. This behavior can be overridden by explicit direct I/O requests
  Buffercachecap – This indicates the maximum amount of memory that can be used for client buffercache
  Cachebufsize – This setting determines the size of individual cache buffers this size also reflects the I/O size when reading and writing through the buffer cache
  buffercache_readahead – Indicates the amount of read-ahead to do when sequential reads are detected
  buffercache_iods – Indicates the number of worker threads created to handle buffered I/O requests