## Slide 1
Lattus-X A10 TOI
Brent Petit
17 JUL 2013
Notes: © 2008 Quantum Corporation. Company Confidential. Forward-looking information is based upon multiple assumptions and uncertainties, does not necessarily represent the company’s outlook and is for planning purposes only.
1

## Slide 3: Lattus-X A10 Overview
The A10 is the Lattus-X Access node
  Provides NFS and CIFS/SMB access to Lattus
    2x 10Gb Ethernet for NFS/CIFS access
  Migrates ingested data out to Wide Area Storage based on snpolicy configuration
    2x 10Gb Ethernet for WAS access
  Provides Vanilla NFS stack via CentOS 6.3 Distribution
    Supports NFSv3 and NFSv4
  Provides Samba stack via Centrify Enabled Samba
    Provides SMB1 and SMB2

## Slide 4: Lattus-X A10 Overview
Hardware
  Dual Xenon CPU
  256GB of Memory
  Boot Volume
    1TB (RAID1, 1+1)
  SNFS Volumes
    2x ~9000GB Volumes (RAID6, 10+2)
      2x 1.4TB SNFS Metadata (2.8TB Total)
      2x 800GB SNFS DR FS (1.6TB Total)
      2x 6TB SNFS Data (12TB Total)

## Slide 5: Lattus-X A10 Overview
WAS Policy driven by snpolicyd
Two SNFS file systems configured
  snfs1 – User Data with WAS policy
    12TB of space for user files
  snfsdr – Holds metadump and database files
    1.6TB of space for DR files
    Metadumps and database backed up to Lattus via snbackup
User file system configures buffercachecap to 224000 (megabytes)
  Lots of buffer cache – trying to move data to Lattus before pushing it out of the client buffer cache

## Slide 6: Lattus-X A10 Overview
NFS
  Standard RedHat/CentOS components
CIFS
  Centrify enabled Samba
    This is different from the full Centrify Suite
  Standard Samba component with enhancements for connecting to Active Directory
  Support RFC 2307 – UID/GID mapping

## Slide 7: Lattus-X A10 Overview
Centrify enabled Samba
  Separately installed package
  Instructions for installation and configuration are in the A10 install guide
Checking connectivity
  /usr/share/centrifydc/bin/adcheck <domain>
    Runs through a series of configuration and connectivity checks
    Is the Centrify software installed correctly?
    Do the configuration files look reasonable?
    Can the host connect to the Domain Controller?
    Is DNS working correctly?
Updating configuration
  /usr/share/centrifydc/bin/adbindproxy.pl
  Script prompts for needed input (Domain, DNS)
  Sets up Active Directory connection

## Slide 8: Lattus-X A10 Overview
Centrify enabled Samba
  Active Directory not required
  Samba can be set up to use smbpassword
    See the A10 Install guide for details
  Lattus-X Install media includes a “Lattus_users.sh” script to automate adding users to the smbpassword file

## Slide 9: Notes
Exporting the same directory with both NFS and Samba is not currently supported
  Due to impact of differing permissions models
Do not set truncation time to zero
  NFS does not keep files open on the server
  Note: this extends beyond A10 to NFS and managed directories

## Slide 10
When in doubt… Review the A10 install guide
  There are pretty explicit instructions for most pieces of the install and configuration
A10 install guide also gives guidance on how to configure NFS clients

## Slide 11
Questions?