## Slide 1
Yingping Lu
July 17, 2013
Lattus-X A10 to M662 Migration Procedures

## Slide 2: What is Lattus-X (Trek)?
Quantum’s first offering to WAS Storage
Includes fast and durable Lattus WAS storage system
Leverage the snpolicyd mechanism to handle file ingesting, storing/fetching/deleting to/from Lattus storage
  Need to configure was storage configuration either via GUI (recommended) or edit /usr/cvfs/config/was.conf
  Define WAS-enabled snpolicy named policy and then assign to the directory that intends for Lattus storage
  Require snfs_was license
Provides NAS accesss (NFS and SAMBA) interfaces to customers

## Slide 3: Lattus-X Architecture
Samba
NFSd
SNFS
SNPD
libcurl
A10
Applications
C10
C10
C10
S10
S10
10Gb links
1Gb links
HTTP REST

## Slide 4: What is Lattus-M (ibis)?
Quantum’s second offering to WAS Storage
Leverages powerful, durable Lattus WAS storage system
Integrates tightly with Stornext Manager product
  Need to configure was storage configuration either via GUI (recommended) or use fswascfg utility
  Storage manager is responsible for storing/fetching/deleting objects to/from Lattus Storage
  Require snsm_was license
Provides a new low latency, durable policy-based tier of storage
Notes: Frank will give more info

## Slide 5: Conversion Overview
Goal
  Migrate the snpolicyd managed files on A10 to M662
  Convert the snpolicyd managed files to SNSM managed files on M662
Tasks
  Prepare migration on A10
  Migrate the snpolicyd-managed files to M662
  Perform conversion on M660
  Post-conversion processing
Documentation
  Lattus-X A10 Migration Procedures

## Slide 6: Prepare Conversion on A10
Stop Ingesting new data to A10
Ensure no ingest backlog on A10
Ensure all files have been uploaded
Handle file system name conflict
Collect snpolicyd-managed dirs and WAS configuration
Generate metadump
Backup migration files

## Slide 7: Stop Ingesting New Data to A10
Stop applications that write to A10 NAS storage
Stop centrify service if present
  service centrifydc –samba stop
Stop NFSD
  service nfs stop

## Slide 8: Ensure Ingest backlog on A10 processed
Set snpolicy parameter was_min_size to 0 if it was set to non-zero value.
  Snpolicy –updatepolicy=mnt_pnt –name=pol_name -policy=was_min_size=0
Regenerate ingest event
  Snpolicy –reingest=src_dir
Wait till all new ingest backlog has been processed
  Snpolicy –policystate=mnt_pnt

## Slide 9: Handle file system name conflict
Unmount and stop snpolicy-managed file system
  umount /stornext/snfs1
  cvadmin –e “stop snfs1”
Change file system snfs1’s configuration file /usr/cvfs/config/snfs1.cfgx
  From <snPolicy>true</snPolicy> to <snPolicy>false<snPolicy>
Run cvupdatefs to change file system name
  cvupdatefs –R snfs2 snfs1
Create a new mount point /stornext/snfs2, replace snfs1 with snfs2 in /etc/fstab
Set parameter snPolicy back to “true” in snfs2.cfgx
Start snfs2 file system and mount it
Notes: If there is a snfs1 file system already exists on M662, a file system name conflict occurs. This step is skipped if no file system name conflict.

## Slide 10: Collect config information
Create a backup dir: /stornext/snfsdr/migration
Copy config files to the backup dir:
  /usr/cvfs/config/snfs1.cfgx (snfs2.cfgx if renamed)
  /usr/cvfs/config/was.conf
  /stornext/snfs1/.rep_private/config/*
Obtain snpolicy managed directories
  Snpolicy –listpolicies=/stornext/snfs1
  By default, /stornext/snfs1/data1

## Slide 11: Generate a new metadump
Stop snfs1
  cvadmin –e “stop snfs1”
Run snmetadump to generate a new metadump
  Snmetadump –dc snfs1
Start snfs1
  cvadmin –e “start snfs1”
Run snmetadump to optimize metadump
  snmetatadump –a snfs1

## Slide 12: Store migration tar file to Lattus storage
Copy metadump file to the migration dir created before.
  /usr/adic/database/metadumps/metadump.snfs1
  /usr/adic/database/metadumps/snfs1.usage
Compress the migration directory
  cd /stornext/snfsdr
  Tar czf migration_snfs1.tgz migration
Backup to Lattus storage
  Found was_id and namespace by running “snpolicy –dumppol=/stornext/snfs1 –name=_snpolicy_backup”
  Found access port from was.conf based on the was_id
  /opt/quantum/curl/bin/curl –T /stornext/snfsdr/migratiom_snfs1.tgz http://192/168.10.1:8080/namespace/NS_backup/migration_snfs1.tgz.`hostname`

## Slide 13: Perform Conversion on M662
Preparation: Connectivity, license
Place M662 to HA config mode
Retrieve backup files from Lattus storage
Resize the metadump
Restore metadump
Add new data stripe group
Configure SM WAStorage
Configure SM policy class
Notes: Require snsm_was license is required for the M662, make sure M662 can access Lattus

## Slide 14: Perform Conversion on M662 (cont.)
Run conversion utility
Perform snpolicyd cleanup
Test the conversion
Bring M662 nodes to HA normal state
Cleanup on the A10 node
Upgrade Lattus to latest version

## Slide 15: Place M662 to HA config mode
Determine the primary node
  Snhamgr status
Run snhamgr config command
  Snhamgr config

## Slide 16: Retrieve backup files from Lattus
Use curl or fsmedread command to get back the stored file
  /usr/adic/TSM/util/fsmedread –u http://192.168.10.1:8080/namespace/NS_backup/migration_snfs1.tgz.A10-hostname /usr/adic/TSM/tmp/migration_snfs1.tgz
Unzip and untar the compressed file
  Cd /usr/adic/TSM/tmp
  Tar xvfz migration_snfs1.tgz

## Slide 17: Resize/Restore the metadump
Copy back snfs1.cfgx to /usr/cvfs/config
Find proper luns for metadump stripe group
  Snfs1 on A10 uses two luns each of size 1434GB
  Snfs1.usage has the current usage of metadata
Update file system config file snfs1.cfgx
  Replace the disk type for A10 with new disk type
  Replace the disks for metadata stripe group
  Set snPolicy to “true”
Run snmetadump to resize metadump
  Metadump –a –s –m –f /usr/adic/TSM/tmp/migration/metadump.snfs1
Restore metadump
  Snmetadump –r –f /usr/adic/TSM/tmp/migration/metadump.snfs1 snfs1

## Slide 18: Add new data stripe group
Add a disk type for the new disk in snfs1.cfgx
Add a new stripe group for the user data
Run cvupdatefs to update file system’s geometry
  cvupdatefs snfs1

## Slide 19: Migration post processing
Shutdown snpolicyd
Update snfs1.cfgx so the original data SG is set to “down” state, write to “false”, set parameters “storageManager” “restoreJournal” to “true”.
Add snfs1 to /usr/cvfs/config/fsm
Edit /etc/fstab to add snfs1 entry
Create a new mount point for snfs1
Start file system snfs1 and mount
Copy back the policy config file
Run snpostrestore to remove files not managed by snpolicyd
  snpostrestore –r /stonext/snfs1

## Slide 20: Perform conversion
Configure SM WASStorage
  Obtain config info from backup file was.conf on A10
  Run fswascfg to configure
Configure a SM policy class
Run convert utility
  Fsaddrelation –c …
Notes: Frank will give more details on the conversion

## Slide 21: Perform snpolicyd cleanup on M662
Remove policy from snpolicyd managed directory
  Snpolicy –removepolicy=/stornext/snfs1/data1
Remove original backup content
  snpolicy –removepolicy=/stornext/snfs1/.SNPOLICY_INTERNAL_BACKUP
  rm –rf /stornext/snfs1/.SNPOLICY_INTERNAL_BACKUP
Remove snpolicy-managed policies
  rm –rf /stornext/snfs1/.rep_private/config/*
Disable snpolicy by setting parameter snPolicy to “false” in snfs1.cfgx
Restart snfs1 file system
  cvadmin –e “stop snfs1”
  cvadmin –e “start snfs1”

## Slide 22: Test conversion
Run fsfileinfo to check file status
Run md5sum to retrieve file content
Verify snbackup is working properly

## Slide 23: A few more steps
Bring M662 nodes to HA normal state
  Run: /usr/cvfs/bin/snhamgr start
Cleanup on the original A10 node
  Decommission or repurpose
Upgrade Lattus to latest version
  Follow Lattus upgrade procedure

## Slide 24: The End
Questions?