## Slide 1
StorNext Connect
“John Koniges”
Customer Install debugging
April 21st & April 22nd, 2015
Mendota Heights

## Slide 2: Customer Install overview
The parts that install and configure a StorNext Pro Solution.
  http://stornextconnect.quantum.com
  Bootstrap
  SNC Installer
  Customer Install
The other parts that customer install uses to complete
  Connector
  StorNext GUI API
  QXS API
The steps that are part of a Customer Install
How to examine your install once completed

## Slide 3: Defining Parts of Customer Install
Terms
  http://stornextconnect.quantum.com
  Bootstrap
    The mechanism for which load our package that includes all of StorNext Connect
    All of the code for this is pre-loaded on appliances and expects a tar.gz package
  SNC Install
    The Mechanism for which our package is installed.
    All of the code for this step is included in the package and executed in two parts
      Part 1 Installs binaries needed by connect through a shell script
        This also configures Apache’s vhosts
      Part 2 is triggered when the first http request hits the connect site
        Database is installed
        User inserted into the database
        StorNext Connect Applications are installed
  Customer Install
    Starts once you see the Customer Install Overview

## Slide 4: Customer Install Parts
Quantum Connector
  Service running on MDCs
  Communicated with via ZMQ
  Runs Python scripts
    Use callback to system
      /opt/quantum/connector/etc/connecthostname contains address for connect
StorNext GUI Webservices
  API layer on top of existing StorNext GUI
  Called from POST, GET URLs
  JSON based returns from GUI
QXS API
  Called from URLs with authentication in header
  URLs same format as command line with / in place of spaces
  Returns XML document

## Slide 5: Customer Install Steps – Behind the scenes
EULA
  Also sets Apache ports to *:80 and restarts Apache
    Default ports are only 169.254.21.2:80
Cables for detection
  Updates Quantum Connector on node 2
  Configures connecthostname to 169.254.21.2
Customer Settings
  Configure Node 2’s Management Network (eth1<M440> / Bond1:2 <M660>)
  Will attempt to use the entered IP Address, Gateway and Netmask
  Will configure DNS for Node 2
  Will validate the Gateway defined with arping.
  Will validate IP addresses to make sure they are available (QXS / Node 1)
  Will Resolve hostnames and then validate services to exist (dns, ntp, etc…)
  Will display all the settings that have been saved, and give the user a chance you go back and change them if they are incorrect.
  Set up bond0:3 as temp bonding on 10.0.0.1 for tmp QXS communication
Bonding M660 Only
  Nothing behind the scenes

## Slide 6: Customer Install Steps – Behind the scenes
QXS Disk Setup
  Verify connection between node 2 and QXS Controller A
  Verify QXS disk count and disk health
    If more than 1 QXS array, this is where it will detect unbalanced arrays
  Set QXS Controller B’s IP address
    Will query A to determine if Controller B’s IP is set correctly.
  Verify Controller B’s IP address via ping
    Out Node 2, in QXS Controller B
  Set QXS Controller A’s IP address
    Will query B to determine if Controller A’s IP is set correctly.
  Verify Controller A’s IP address via ping
    Out Node 2, in QXS Controller A
  Set QXS NTP, Hostname
QXS Disk Provision
  Calls one button install once per enclosure at 10+2 configuration
If multiple Arrays, repeat for each

## Slide 7: Customer Install Steps – Behind the scenes
Node 1 Management Network
  Remove bond0:3 tmp bonding used for QXS
  Configure Node 1’s Management Network (eth1<M440> / Bond1:2 <M660>)
  Verify IP address was set by pinging Node 1 from Node 2
Node 2 Metadata Network
  Configure Node 2’s Metadata Network Bond0:2
Node 1 Metadata Network
  Configure Node 1’s Metadata Network Bond0:2
  Verify IP address was set by pinging Node 1 from Node 2

## Slide 8: Customer Install Steps – Behind the scenes
Cable Fibre Channel
  Send GUI settings to GUI on both nodes
  Force NTP to sync
  Add hostname to /etc/hosts for paired MDC
  SCSI rescan
  Validate SAS / fiber cables
  Setup VIP on MDCs
  Restart Mintd
  Restart Syslogd
  Restart Hwmond
  Restart snapism
  Restart Sendmail
  Restart StorNext GUI
    Wait for StorNext GUI to respond again

## Slide 9: Customer Install Steps – Behind the scenes
HA Pair
  Make sure license on Node 1 has information for both nodes
  Convert Node 1 to HA Pair
  Convert Node 2 to HA Pair
Create Volume(s)
  Trigger cvadmin rescan
  Validate all LUNs exist
    Metadata
      M44X 2 (4 w/ expansion)
      M660 8 (16 w/ expansion)
    Validate both MDCs can see all QXS LUNs
  Send message to GUI to create volume(s)
    Repeat for each volume

## Slide 10: Customer Install Steps – Behind the scenes
Configure Library (if exists)
  Send command to StorNext GUI to list all Libraries visible over Fibre
  Iterate over list to find a match with the serial number specified in BOM
  Send a message to the StorNext GUI add the given library
    DNS must resolve correctly for Node 2’s management IP
      The AEL i500 will try to communicate back to the node via Ethernet
    Control path must be configured on the AEL i500
  After Library is added we send a generic policy to the StorNext GUI
    Should modify policy for specific needs
Customer Install Complete
  We enable all StorNext Connect apps, disable Customer Install
    Starts supervisord managed workers that monitor beanstalkd
  Configure cron to run for StorNext Connect
  Start carbon-cache with supervisord
  Add setting to database that Connect has completed the Install
    Enables Dashboard
  One final restart of Apache

## Slide 11: View Install history
Manage Other Components

## Slide 12: View Install history
Manage Other Components

## Slide 13: View Install history
Manage Other Components

## Slide 14: CI Log – <connect ip|169.254.21.2>/install-pro/logs
[0109 12:53:30-0600] fatal - cable-detection - Connector - failure - Command completed - Installed client release (51487) did not match expected 1.0.0
**Std out: {
"snconnect_client": {
"version": "1.0.0",
"graphite_host": "10.1.1.2",
"components": {
"connector": {
"release": "602.1",
"version": "1.0.0"
},
"mintd": {
"release": "51487",
"version": "1.0.0"
},
"snupdate": {
"release": "604.1",
"version": "1.0.4"
},
"connectplugins": {
"release": "51487",
"version": "1.0.0"
},
"service_router": {
"release": "537.4",
"version": "0.1.0"
}
},
"snchostname": "10.1.1.2",
"release": "51487",
"graphite_port": "2004"
}
}
**Std err:
**error code: 0
[0109 12:53:30-0600] fatal - cable-detection - Customer Install - failure - - cable-detection failed with the following error: Installed client release (51487) did not match expected 1.0.0

## Slide 15: Reference
http://php.net
http://supervisord.org/
https://www.python.org/
http://zeromq.org/
http://czmq.zeromq.org/
https://developers.google.com/protocol-buffers/

## Slide 16: Q&A