## Slide 1: LTO Advanced Path Failover
Architectural Overview
Curtis Ballard / July, 2013

## Slide 2: Why is tape path failover hard?
A bit of background on tape and SCSI
Tape Read/Write model
SCSI Architectural Model

## Slide 3: Tape Read/Write model

## Slide 4: The tape read/write model
Tapes are ‘sequential’ devices – data is accessed in sequence, not random
Data on tape is not addressed by a specific position
  Addresses exist but are rarely used and aren’t supported at all for read or write commands
  Applications mark data boundaries using filemarks and typically index using those marks
New data is written ‘Here’
  ‘Here’ is whatever the current position happens to be
  The WRITE command does not contain an address for where the data should be written
  Applications usually don’t know exactly where the data was written
Data is also read from ‘Here’
  Whatever data is under the head is returned when a READ is requested

## Slide 5: Path failures can result in several conditions
Command to write ‘Data-3’ was dropped due to a path failure
Nothing was written, head is still positioned at start of data
Command to write ‘Data-3’ was dropped due to a path failure in the middle of data transfer
Part of the data was written, EOD is missing, head is positioned somewhere in the middle of the data
Command to write ‘Data-3’ was dropped due to a path failure after completion of data transfer
  All of the data was written, EOD may or may not be written yet, head is positioned at the end of the data

## Slide 6: Resending a command can result in data corruption
Unless the command never got to the drive, it can’t be resent safely
Since the data is accessed at the current head location a simple command retry results in data corruption due to unexpected data on the tape.
Example shown for the ‘Partial Write’ case
Driver detect path failure and retries command on another path

## Slide 7: Not handled with disk path failover solutions
Path failover solutions to disk are common
Disk path failover assumes that it is always safe to simply resend a command because all disk access commands contain addresses
The driver doesn’t have to know about head/media position or perform any recovery – the storage device can use the address information in the command to position the head/media before performing the command.

## Slide 8: SCSI Architectural Model

## Slide 9: A SCSI Device view of the world
The target devices don’t see what you might expect
The SCSI Architectural Model (SAM) defines SCSI devices as Initiators and Targets
  Initiators send commands and receive responses
  Targets process commands and transmit responses
Both initiators and targets contain ‘ports’ – the device through which the devices connect
  Almost always associated with the physical port
SCSI communications occur between an ‘Initiator port’ and a ‘Target port’
  This connection is commonly called a ‘link’ or a ‘path’
  The SCSI term for this Initiator to Target path is an “I_T nexus” or ‘nexus’ for short
  Most SCSI information is local to the path and owned by the path
  Settings on one path can affect another but most can’t directly be controlled by another path
Every port has a different identifier so the target devices sees each path as a path to another initiator
The target device can not associate ports with hosts

## Slide 10: Our view of a SCSI configuration
Single host, multi-path, multi-SAN
  Host
    One Device
    Several paths to that device
  Device
    One Host
    Several paths to that host

## Slide 11: Device view of the same SCSI configuration
The device sees multiple initiators
  Logical view
    One Device
    Several Initiators connected
      to that device
  The SCSI architectural model requires the drive to treat each path as a (mostly) independent connection.

## Slide 12: Advanced Path Failover

## Slide 13: High Level Diagram

## Slide 14: Most failover solutions
  Device Driver
      Detect multiple paths to devices
      Only present single path to OS
      Performs all failure detection and recovery
      Including managing connection specific settings
    Target Device (tape drive and/or library)
      Unaware of failover
      Provides basic SCSI mechanisms for exception condition recovery

## Slide 15: APF is a cooperative solution to path failover
  Device Driver
      Identify duplicate paths to device
      Select a preferred path
      Only present one path to OS
      Establish a failover connection on the preferred path
      Use another path to notify device of path switch following failure
    Target Device (tape drive and/or library)
      Accept failover connection on any path
      Perform command cleanup when notified of a path switch
      Track the failover connection across path switches
      Manage settings transfer automatically upon path switch

## Slide 16: Basic Concepts

## Slide 17: Failover Restricted Commands
  Only a few SCSI commands require recovery
    Many commands can be safely retried, even if they cause a state change
      Examples:
      Inquiry – no state change, safe to retry
      Reserve – requesting a reservation when holding a reservation is a No-Op, safe to retry
      Many other similar commands either do not change state or sending twice results in the desired state
    Other commands can leave the system in an indeterminate state
      Write – partial or full write moves the head/media position (see previous example)
      Locate – moves the head/media position even though no data was transferred
      Move Medium – changes the position of tapes in the library
    Commands that leave the system in an indeterminate state are called ‘Failover Restricted Commands’ and are tracked

## Slide 18: Failover Sequence Counter
  Used to track Failover Restricted Commands
    Every SCSI command has 2 bits that are available for ‘Vendor Specific’ use
    Commands for tape drives and libraries that change the state are sent one at a time
      Only one Failover Restricted Command in process at a time
      Normal operating model but enforced by failover drivers
    With one command at a time in progress there are only three possible states:
      Command not yet received
      Command is in progress
      Command has completed
    The 2 vendor specific bits are used to create a 3 step counter – the Failover Sequence Counter
    Counter is incremented for every command, rotates through 1,2,3
    Both the device driver and the target device can identify the failover restricted command using the counter
    A counter set to 0 means the device driver does not support failover and the device rejects the command

## Slide 19: Failover Sessions
  SCSI target devices can’t tell that different paths come from the same host
  APF defines ‘Failover Sessions’ as the method for the target device to identify hosts
    Device driver creates a 4 byte ‘Failover Session Key’
      Passes the session key to the target device in a ‘Session Request’ command to create a ‘failover session’
      Target device accepts the key if it is unique or tells driver to try again in case of conflict
      Target device associates the session key with the path over which it was received
      All device settings (reservations, etc) created on that port are associated with that session key
    Following a path failure the device driver connects using another path
      Sends a command to notify the target device that a path switch is occurring (A Nexus Change)
      Passes the Failover Session Key to the target device to tell the device which host is switching paths
      Target device looks for a matching Failover Session Key and if found transfers all settings to the new path

## Slide 20: Device SCSI configuration view with failover sessions
Single host, multi-path, multi-SAN
  Host
    One Device
    Several paths to that device
  Device
    Several paths
    One failover session
    Each path using that failover session is the same host
Shared Failover Session Key

## Slide 21: Nexus Change Notification
  A method for the device driver to notify the target device of a path change
  The synchronization tool for command recovery
    The ‘Nexus Change Notification’ provides all the information the target device needs for synchronization with the failover device driver
      Contains the Failover Session Key to identify which host is performing failover
      Includes information about whether the host that is performing failover had an outstanding command
      Provides failover sequence counter value if a failover restricted command was outstanding
    Target device processes the Nexus Change to determine what synchronization is needed
      Uses the Failover Session Key to identify which host is performing failover
      If a failover restricted command was outstanding, checks the failover sequence counter
        Command may not have been received yet, no action
        If command is in progress or has been completed, backs out the changes (drive) or completes cmd (lib)
        If command can’t be backed out (e.g., ERASE), notifies the device driver
      Reports synchronization success or failure back to the device driver

## Slide 22: Example Failover Session

## Slide 23: Device Discovery
Device driver:
The device driver probes devices as the operating system discovers them
  Reads the device World Wide Node Name (WWNN)
  All devices that report the same WWNN are considered to be the same device
  For tape libraries also determines which paths address an active control path drive
  Exact method is OS specific
Creates OS visible device when first path is discovered
Adds new paths to known devices to an alternate path list
Operating system notifies device driver of device connection (boot or scan)

## Slide 24: Create Failover Session
Device driver:
When first device access is needed
  Create Failover Session Key
  Request failover session
  If successful store failover session key
Target Device:
Process Failover Session Request
If key is already known and not from this host, report ‘different key needed’
If too busy to create a new session return ‘Busy’
Associate session key with path over which key was received

## Slide 25: Monitor Commands
Device driver:
When a command is received, test for whether command is failover restricted
  Not restricted: pass on command as received
  Restricted: Insert Failover Sequence Counter
Target Device:
When a command is received, test for whether command is failover restricted
Not restricted: process command normally
Restricted: validate Failover Sequence Counter
  Test for next counter in sequence
  Reject invalid or missing counter values (code bug or non-failover driver)

## Slide 26: Normal Command Completion
Device driver:
When a command response is received
  If command was failover restricted, increment Failover Sequence Counter
Return command status to application
  Command may have complete successfully or returned an error
Target Device:
When command status is transmitted
  If command was failover restricted, increment the Failover Sequence Counter
Low overhead in normal operation – performance is nearly identical to non-failover

## Slide 27: Path Failure Detected
Device driver:
OS notification received for path failure
Check device path list for alternative paths
  Send low overhead verify path command to test other paths
  If medium changer path
    try to find path to active control path drive
    if required, send command to activate passive control path drive
If valid alternative path is identified change active path
Send ‘Nexus Change Notification’ to the target device to notify it of path failure

## Slide 28: Path Failure Detected, cont.
Target Device:
When a Nexus Change Notification is received
  If restricted command was lost
    Compare failover sequence counter of lost command to most recent command
    If command wasn’t received yet, no action
    If command is in process:
      Tape Drive: back out the command and return tape/head position to same position as at the start of that command
      Tape Library: complete command, save the command and results
Transfer all settings associated with the identified failover session to the path over which the nexus change command was received
Return status when synchronization is complete

## Slide 29: Path Change Successful
Device driver:
Resend original command
Target device:
Tape drive:
  process command normally
Tape library:
  Compare command to saved command
    If command matches, report saved results
    If command doesn’t match, report error (driver code bug)

## Slide 30: Special Steps for Libraries
Issue:
Libraries can’t identify host ports so reservations and prevent medium removal is handled entirely in the drive hosting the path
Two drives host a path to the same library
  Drives do not have a communication link
  Driver enforces all accesses through one drive, the ‘active control path drive’
  Passive control path drive also limits access
  All reservations and prevent medium removal settings are held by the ‘active control path drive’
If active control path drive fails, must be able to change path to another drive
  Passive control path drive doesn’t know about the reserve/prevent settings

## Slide 31: Special Steps for Libraries, cont
Handling this issue:
Device driver
  Monitor for commands that cause settings change
  After command that can cause settings change query library path for whether settings did change
  If settings changed read a cache of the settings from the drive hosting the path
  If active control path drive is changed, transfer the settings cache to the new drive
Drive hosting library control path
  Monitor library settings for changes for any reason (not only commands)
  After library settings change occurs, set notification for host
  Support commands to report cache of settings hosted for library
  Support commands to receive cache and establish those settings in this drive

## Slide 32: Special Steps for Libraries, cont
Solution is imperfect
  leaves small window where path failure during settings transfer causes incomplete transfer
Same potential exists with today’s basic path failover
Providing host utility and (hopefully) function in library to reset reservations
Working on methods to narrow the possibility in future releases
Imperfect solution is still better than existing non-failover environments
Multipath software can leave ‘stranded reservations’
  Reservation established
  Path failure – at any time – causes path change
  Reservation on previous path is ‘stranded’