## Slide 1: Advanced Path Failover Training
22 July 2013

## Slide 2: NEW dial-in information
1-866-692-4541
Participant code: 8586201

## Slide 3: Overview
Goals
Windows driver architecture
Demonstrations
Utilities
Documentation review

## Slide 4: Overview
Goals
Windows driver architecture
Demonstrations
Utilities
Documentation review

## Slide 5: Goals
Hide SAN or device failures from applications
Primum non nocere
  (First, do no harm – failure conditions must be no worse than without APFO)
Can’t fix an unstable system

## Slide 6: Overview
Goals
Windows driver architecture
Demonstrations
Utilities
Documentation review

## Slide 7: This is your stack

## Slide 8: Windows driver architecture
Windows APFO driver consists of one filter driver and one intermediate class driver
Fit below miniclass drivers (tape and changer) and above port driver

## Slide 9: This is your stack on APFO

## Slide 10: tapeusbf filter driver
Attaches to all storage port drivers
During discovery recognizes devices which may have APFO capability
Presents a FFDO and FPDO for each path to each device
FFDO and FPDO identifiers are recognized by tapempic
Notes: 2nd & 3rd bullet items are modified from what was shown in the presentation

## Slide 11: tapempic intermediate class driver
Attaches to devices presented by tapeusbf
Presents a FDO and PDO for each enabled device to the tape and media changer miniclass drivers above
Performs the APFO functionality:
  Manages failover sequence counters (FSCs)
  Manages failover session keys
  Passes commands to devices, modified as required
  Changes path when a failure occurs

## Slide 12: Device objects
Windows manages devices using …
  Physical Device Objects (PDO)
  Functional Device Objects (FDO)
Filter drivers add FPDOs and FFDOs
tapempic selects active path
Notes: CDO provides an API for the diagnostic application

## Slide 13: Overview
Goals
Windows driver architecture
Demonstrations
Utilities
Documentation review

## Slide 14: Demonstrations
Configure library
Install drivers on host
Fail switch port to trigger failover
Fail drive to trigger failover
Utilities

## Slide 15: Configuration guidelines
Configure APFO in library first
Install APFO drivers in hosts second
  When updating from pre-release to release drivers, manually uninstall pre-release drivers first.
Cannot mix basic and advanced failover within a partition
Notes: If enable library then boot host w/o drivers, half of the changers will not load a changer miniclass driver. Caused by reservation conflict in passive control path drives. Exclamation points in device manager display. Solution is to install APFO drivers and reboot.

## Slide 16: Library configuration
Enable storage networking (SNW) license
Set up partitions
Select control path drives
Select data path drives
Verify host access
See User’s Guide

## Slide 17: SNW license

## Slide 18: Licenses

## Slide 19: Partitions – configure
Setup >> Partitions >> Configure

## Slide 20: Configure control path
Setup >> Partition >> Control Path
  Select CP Drive
  Select CFP Mode: Advanced
  Select Passive CP Drive
Notes: Enable both drive ports in Security Manager.
Yellow is active CP drive

## Slide 21: Configure data paths
Setup >> Drives >> Data Path Failover
  Select Partition
  Select Drives and enable ADPF
Notes: Enable both drive ports in Security Manager.

## Slide 22: Configure host access
Setup >> Drives >> Access >> SNW Wizard
  Host Access
    Host Access Group configuration
    Host Access Configuration
  All drives in a partition must use either basic or advanced failover; no mixing.
Notes: Enable both drive ports in Security Manager.

## Slide 23: SNW Wizard – host access

## Slide 24: SNW Wizard – host access options

## Slide 25: SNW Wizard – groups
Notes: Security Manager

## Slide 26: SNW Wizard – drive access
Notes: Selected ports will be available to all hosts selected at this point.

## Slide 27: SNW Wizard – host access

## Slide 28: Driver installation
Limited distribution; not on Quantum web site
Pre-release drivers must be uninstalled manually before upgrading to newer drivers
Single installer application for both drivers
  Windows 2012 Server
    advfo2K12.exe
  Windows 2008 Server x64 and 2008 R2 Server
    advfox64.exe
    32-bit (x86) Windows 2008 is not supported
C:\Program Files\Quantum\Failover\
Driver signatures
  Released drivers will be signed by Microsoft
  Using a test signed driver requires putting Windows in test mode
Notes: Quantum presentation only
Win 2012 x64 only, hence name
Put in test mode first, else attempt to boot will enter recovery mode
“bcdedit testsigning on” and reboot

## Slide 29: System topology
One server with two HBAs
One switch with two zones
One library with a partition containing two drives
Each drive has two ports and is configured for bridging
Each drive contains an SSC and an SMC device server
Notes: This will help explain the Device Manager view which will have sixteen instances of “AdvFO Tape Multi-Path Intermediate Class Driver SCSI FDO.”

## Slide 30: Device manager
Notes: Multiple instances of the library or of each drive indicate that APFO is not enabled in the library.
Eight changer, eight drives
Replace this with screen shot from Louie

## Slide 31: Failover demonstration

## Slide 32: Diagnosis
Objective: Restore failed link or drive before the redundant element fails.
Identify the failed element
  Link or drive?

## Slide 33: Data and control path failover

## Slide 34: Control path failover across drives

## Slide 35: Diagnosis process
Library RAS tickets
Windows system event log
Diagnostic application
Debug (checked) drivers to generate debug logs
Crash dumps to debug BSODs
Notes: Ask service people how much of this should be given to customer and how much to give only to field service
Debug drivers will be signed

## Slide 36: RAS ticket available

## Slide 37: RAS ticket list

## Slide 38: RAS ticket details
Notes: Coordinates of failed element

## Slide 39: RAS ticket report

## Slide 40: Windows event log
Event | Severity | Message
Driver loaded | Informational | “Path failover driver loaded”
Driver unable to load | Error | “Path failover driver unable to load”
Path failure detected | Error | “Path failure detected on SCSI Port %s Bus %3 Target Id %4 Logical Unit %5”
Failover session established | Informational | “Failover session established on SCSI Port %2 SCSI Bus %3 Target Id %4 Logical Unit %5”
Failover session establishment error | Error | “Failover session establishment error on SCSI Port %2 SCSI Bus %3 Target Id %4 Logical Unit %5. Reason code %6.”
Hint: Filter current log event sources for tapeusbf and tapempic.

## Slide 41: Event log – driver loaded

## Slide 42: Event log – session established

## Slide 43: Event log – path failure
Notes: Check AdvFoDgn to see which drive is missing a path

## Slide 44: Overview
Goals
Windows driver architecture
Demonstration
Utilities
Documentation review

## Slide 45: Utilities
AdvFoDgn – failover session states and device names
Crash dumps for debugging BSODs – see Customer Essentials
Notes: Quantum version

## Slide 46: AdvFoDgn diagnostic
Shows states of failover sessions
Shows names of devices
Communicates with the driver
Some ISV applications may need to use symbolic names of drives and changers.

## Slide 47: AdvFoDgn display
Notes: Bottom pane is driver state

## Slide 48: AdvFoDgn actions
Show WWN
Report Device
  Enabled
  Session Status
  Session List
Report Local SMC
  Legacy Reservations
  Prevent Media Removal
  Persistent Reservations

## Slide 49: AdvFoDgn device enabled status

## Slide 50: AdvFoDgn device session status

## Slide 51: AdvFoDgn device session list

## Slide 52: AdvFoDgn SMC legacy reservations

## Slide 53: AdvFoDgn SMC prevent removal

## Slide 54: AdvFoDgn SMC persistent reservations

## Slide 55: Clearing reservations – AfoClrRs
Some failures may leave a drive or library with a reservation placed by a dead host.
AfoClrRs will clear reservations manually.
Installed along with drivers.
Notes: Will go into AdvFoDgn

## Slide 56: Overview
Goals
Windows driver architecture
Demonstration
Utilities
Documentation review

## Slide 57: References
Advanced Path Failover User Essentials
Release notes (TBD)